## Slide 1
Physical AI: How a Robot Learns
Data Acquisition & Policy Learning · Lesson 1 (Lecture)
Notes: Welcome everyone to the first lesson of Data Acquisition and Policy Learning. Over the next fourteen weeks we are going to teach a real robot arm, the SO-101, to do a useful task: pick up a cube and put it in a bin. We will do it three different ways, and by the end you will understand when each way makes sense.
Today is a lecture. We will not touch code yet. The goal is to give you the vocabulary and the big picture, so that when you sit in front of Isaac Sim and the real arm next week, everything you see has a name and a place.

## Slide 2: Our course map: one cycle, walked three times
Simulate
Collect data
Train
Evaluate
Deploy
Improve
Physical AI
lifecycle
A
Foundations L1–L2
B
Collecting robot data L3–L4
C
RL in simulation L5–L6
D
RL: sim → real arm L7–L8
E
Imitation learning L9–L10
F
Evaluate & deploy IL L11–L12
G
Vision-language-action L13–L14
Notes: This wheel is the map for the whole course, and you will see it at the start of every lecture. Every physical AI project goes round this cycle: we build or use a simulation, we collect data, we train a policy, we evaluate it, we deploy it on the real robot, and then we improve it and go round again.
On the right are our seven blocks. Notice that we do not cover each stage once and move on. We walk the whole cycle once for reinforcement learning, once for imitation learning, and once for vision-language-action models. Each time round, you reuse what you built the last time. Today we are in Block A, the foundations.

## Slide 3: Quick poll
What do you think is hard about getting a robot to do something useful?
Answer anonymously in the poll. One or two words is fine.
seeing?
grasping?
data?
safety?
cost?
Notes: Before I explain anything, I want to hear what you think. Open the poll and type what you think is hard about getting a robot to do something useful. There are no wrong answers. The words at the bottom are only prompts.
Instructor: keep these answers. In Lesson 13 we will come back to them, and by then the class should be able to explain most of them.

## Slide 4: Learning outcomes
By the end of this lesson you should be able to:
  explain how physical AI differs from AI that runs on a screen
  describe the six stages of the physical AI development lifecycle
  name the observation and action of the SO-101 at each control step
  compare reinforcement learning, imitation learning and VLA by where their training data comes from
Notes: Here are the four things you should be able to do by the end of today. Keep them in mind, because the exit ticket at the end checks exactly these four. The last one is the most important: if you can say where each method gets its data, you have the key that unlocks the rest of the course.

## Slide 5: Part 1
From screen AI to physical AI
Why a robot is not just a classifier with a body
Notes: Part one. We start with the question of what changes when AI leaves the screen and has to act in the physical world.

## Slide 6: Screen AI answers once; a robot decides 30 times a second
Screen AI (e.g. image classifier)
Image
Model
“cat”
One input, one answer.
The answer does not change the next image.
A mistake is just a wrong label.
Physical AI (robot policy)
Camera + joints
Policy
Arm moves
World changes
Every action changes the next input.
A mistake moves the robot somewhere new.
Notes: On the left is the kind of AI you already know well. An image classifier sees one picture and gives one answer. Whatever it says, the next picture is not affected. If it is wrong, you just get a wrong label.
On the right is a robot. The policy looks at the camera and the joint readings, decides an action, the arm moves, and the world changes. Then the camera sees the changed world and the policy decides again, about thirty times every second. This loop is the single most important idea today. Everything that makes robotics hard comes from the fact that the robot's own actions decide what it sees next.

## Slide 7: The control loop: perceive → decide → act, every 33 ms
Perceive
read 6 joint positions + camera images
Decide
policy computes the next action
Act
send 6 target joint positions
…and repeat. At 30 Hz there are 30 decisions per second: one every 33 milliseconds.
The policy is the only part we train. Everything else (the sensors and motors) stays the same for every method in this course.
Notes: Let us zoom into that loop. Perceive: the robot reads where its joints are and grabs camera images. Decide: the policy, which is a neural network, turns that into an action. Act: the action is sent to the motors as six target positions. Then it starts again.
On our arm this happens about thirty times a second, so the policy has roughly thirty-three milliseconds to think each time. Remember that the policy is the only part we ever train. Reinforcement learning, imitation learning and VLA models are three different ways of producing that one box in the middle.

## Slide 8: Why physical AI is hard
Errors compound
2 mm off at the start of a grasp can become 2 cm off at the end. Each mistake feeds the next decision.
Data is not independent
Each frame follows from the last. Shuffling frames like images hides how the robot actually behaves.
Mistakes cost money
A bad action can hit the table, drop the object or strain a motor. Testing is never free.
Data is slow
One real demonstration takes about a minute. An image dataset can be scraped; robot data must be performed.
Notes: Because of the loop, physical AI has four problems that ordinary machine learning mostly does not.
First, errors compound. A tiny error early on puts the arm somewhere slightly unusual, the next decision is a bit worse, and by the end of the grasp you have missed. Second, the data is not independent. In image classification we shuffle pictures freely; here every frame depends on the previous one. Third, mistakes cost money and time, because the robot is real. And fourth, data is slow: every demonstration has to be physically performed by someone. Keep these four in mind. Almost every technique in this course exists to deal with one of them.
Instructor: if you have a short clip of a real policy failing, play it here.

## Slide 9: Simulation makes trials cheap, at a price
What simulation gives us
Thousands of robots trying at once on one GPU
Perfect labels for free (exact positions, contacts)
No broken hardware, no safety risk
Faster than real time
What it costs: the reality gap
Dynamics
masses, friction, how the motors respond
Appearance
colours, textures, lighting
Sensing
noise, offsets, delays
Anything the simulator leaves out, the policy never learns about.
Notes: This is why simulation matters so much in robotics. In a simulator we can run thousands of copies of the robot at the same time on one graphics card. We get perfect information for free, nothing breaks, and it runs faster than real time.
But there is a price, called the reality gap. The simulator is a model of the world, not the world. It gets masses, friction and motor behaviour slightly wrong; it renders colours and lighting differently from our lab; and its sensors are cleaner than real ones. A policy trained only in simulation can fail on the real arm because of these differences. We will come back to these three gaps in Lesson 3 and Lesson 7.
Instructor: the parallel-training video on the legged_gym project page works well here.

## Slide 10: Part 2
Robot basics with the SO-101
Joints, spaces, servos and one control step
Notes: After the break we meet the robot we will use all semester.

## Slide 11: Meet the SO-101
PHOTO / VIDEO
Labelled photo of your lab's SO-101 (leader and follower)
1
shoulder_pan rotates the whole arm left/right
2
shoulder_lift raises/lowers the upper arm
3
elbow_flex bends the elbow
4
wrist_flex tilts the wrist up/down
5
wrist_roll rotates the wrist
6
gripper opens and closes the jaws
Open-source design by TheRobotStudio with Hugging Face
Notes: This is the SO-101, a low-cost, open-source robot arm designed by TheRobotStudio together with Hugging Face. It has six motors. Five of them move the arm: the shoulder pan turns the whole arm, shoulder lift raises it, elbow flex bends the elbow, wrist flex tilts the wrist, and wrist roll turns it. The sixth motor opens and closes the gripper.
These six names will appear in every dataset and every config file you open, so it is worth learning them now. Instructor: replace the photo frame with a labelled photo of the arm in your lab, and pass a powered-off arm around if you can.

## Slide 12: Joints, degrees of freedom and workspace
Joint
A place where two parts of the arm connect and can move.
Degree of freedom (DOF)
An independent way the robot can move. The SO-101 has 5 arm DOF plus a gripper.
Workspace
All the places the gripper can reach. Outside it, no policy can succeed.
PHOTO / VIDEO
Short clip: moving one joint at a time
Notes: Three words. A joint is where two parts of the arm connect and can move relative to each other. A degree of freedom is one independent way the robot can move, and our arm has five for the arm plus the gripper. The workspace is every position the gripper can actually reach.
Five degrees of freedom is enough for picking and placing, but it is not enough to reach every point at every angle. A human arm has seven. So sometimes the arm simply cannot hold the gripper the way you want, and that is a hardware limit, not a learning failure.
Instructor: a short clip moving one joint at a time is very effective here.

## Slide 13: Two ways to describe the same pose
Joint space
six joint angles
[ 12°, −40°, 85°, 30°, 0°, 20° ]
Cartesian space
where the gripper is
x, y, z + orientation
Forward kinematics
Inverse kinematics
Forward: “Given how my arm is bent, where is my hand?” (one answer)
Inverse: “How should I bend my arm to reach the cup?” (maybe many answers, maybe none)
Notes: There are two ways to describe what the arm is doing. In joint space, we list the six joint angles. In Cartesian space, we say where the gripper is: its x, y and z position and which way it is pointing.
Going from joint angles to gripper position is called forward kinematics, and it always has exactly one answer. Going the other way, from a desired gripper position to joint angles, is inverse kinematics, and it is harder: there may be several ways to bend the arm, or none at all if the point is out of reach. Think of your own arm: knowing how your elbow and shoulder are bent tells you exactly where your hand is, but reaching for a cup can be done in more than one way. We only need the intuition here, no matrices. Our policies will mostly output joint positions directly.

## Slide 14: Our servos take positions, not forces
We CAN command
A target position for each joint
(the servo's own controller drives towards it)
We CANNOT command
A force or torque
“Grip harder” or “push gently”
Six Feetech STS3215 serial-bus servos. Grip force comes only indirectly, by telling the gripper to close further than the object allows. This limit returns in Lessons 7 and 9.
Notes: One hardware fact that matters a lot later. Each joint is driven by a Feetech STS3215 servo. You send it a target position and its own small controller drives towards that position. You cannot send it a force or a torque.
So if you want the gripper to hold something firmly, the only way is to command it to close further than the object allows, and let it squeeze. Expensive research arms can control force directly; ours cannot. This is one reason some published methods do not work as-is on this arm, and it is one reason imitation learning works so well here. We will come back to this in Lessons 7 and 9.

## Slide 15: Leader, follower and cameras
Leader arm
moved by your hand
joint readings 30× per second
Follower arm
copies the leader
Front camera
sees the whole scene
Wrist camera
sees the grasp up close
Recorded every frame: leader position (the action), follower position (the state), both camera images.
This is how most of the data in this course will be collected.
Notes: Our robot comes as a pair. The leader arm has the same shape as the follower but lighter gearing, so you can move it easily by hand. As you move it, its joint readings are sent to the follower about thirty times a second, and the follower copies the movement. This is called teleoperation, and next week you will try it yourselves.
We also mount two cameras: one in front that sees the whole scene, and one on the wrist that sees the grasp up close. When we record, every frame stores the leader's position, which is the command or action, the follower's position, which is the state, and both camera images. That recording is the raw material for imitation learning.

## Slide 16: Worked example: one control step
Observation (input)
6 joint positions
[ 2.1, −38.5, 81.0, 27.4, −1.2, 18.0 ]
+ front image + wrist image
policy
Action (output)
6 target joint positions
[ 2.4, −37.9, 80.2, 27.9, −1.2, 12.5 ]
180
joint numbers per second
60
images per second
600
frames in a 20 s demo
1,200
images in a 20 s demo
Example values are illustrative; replace with numbers captured from your own arm.
Notes: Let us make this concrete with one control step. The policy receives six joint positions plus two camera images. It outputs six numbers: the target position for each joint. Notice the outputs are very close to the inputs. Each step only nudges the arm a little, which is why it has to happen thirty times a second.
Now the arithmetic. Six joint values thirty times a second is one hundred and eighty numbers per second, plus sixty images. A twenty-second demonstration is six hundred frames and twelve hundred images. In Lesson 3 we will use exactly this calculation to work out how big our dataset needs to be.
Instructor: capture real values from your arm during teleoperation and replace the example numbers.

## Slide 17: Part 3
The lifecycle and three ways to train an arm
Where does the training data come from?
Notes: Final part: how a robot policy actually gets built, and the three families of methods we will study.

## Slide 18: The physical AI development lifecycle
Simulate
Build a virtual robot and scene
Collect data
Demonstrations or trial-and-error
Train
Fit the policy network
Evaluate
Measure success honestly
Deploy
Run it on the real arm
Improve
Fix the main failure, repeat
Simulation helps most at the start. Evaluation and improvement are where most real projects spend their time.
Notes: Here are the six stages in order. We simulate the robot and its scene. We collect data, either by demonstrating or by letting the robot try. We train the policy. We evaluate it honestly, which means counting successes on the real task, not just looking at a loss curve. We deploy it on the real arm. And we improve it by finding the main failure and fixing it, then going round again.
Beginners usually think training is the main event. In practice, most of the time on real projects goes into data, evaluation and improvement. This course is designed to give those stages the time they deserve.

## Slide 19: Three ways to train an arm
Where data comes from
What you provide
Where it trains
Typical failure
Reinforcement learning
Robot tries, gets a score
You write the reward
Mostly in simulation
Fails by reward hacking
Imitation learning
Human demonstrates
You record the dataset
Real arm, no reward
Fails off its training data
Vision-language-action
Demos + a sentence
Fine-tune a big pretrained model
One model, many tasks
Can pick the wrong task
The key question: does the data come from the robot trying, or from a person showing?
Notes: Now the three families of methods, and the one question that separates them: where does the training data come from?
In reinforcement learning the robot generates its own data by trying, and you write a reward function that scores each attempt. That happens mostly in simulation, and its typical failure is reward hacking: the robot finds a way to score well that is not what you meant.
In imitation learning a person demonstrates the task, and the recorded actions are the correct answers. There is no reward at all; it is supervised learning. It trains on real data, and it fails when the robot drifts into situations the demonstrations never showed.
A vision-language-action model is imitation learning on top of a large pretrained model, with a sentence attached to each demonstration, so one model can do several tasks. Its typical failure is doing the wrong task confidently. If you remember only one slide from today, make it this one.

## Slide 20: Course roadmap: 14 weeks
Wk 1
L1
Lec
Wk 2
L2
Lab
Wk 3
L3
Lec
Wk 4
L4
Lab
Wk 5
L5
Lec
Wk 6
L6
Lab
Wk 7
L7
Lec
Wk 8
L8
Lab
Wk 9
L9
Lec
Wk 10
L10
Lab
Wk 11
L11
Lec
Wk 12
L12
Lab
Wk 13
L13
Lec
Wk 14
L14
Lab
Foundations
Data
RL in sim
RL → arm
Imitation
Evaluate
VLA
Test 1
after Week 8 · Lessons 1–8
Test 2
after Week 14 · Lessons 9–14
Assignment
pick-and-place project · demo after Week 14
Lecture weeks explain the idea; lab weeks make it run in Isaac Sim and on the SO-101. Each lesson starts with a short check on the last one.
Notes: This is how the fourteen weeks fit together. Odd weeks are lectures like today; even weeks are three-hour labs where you use Isaac Sim and the real SO-101 arm. Each lab puts the previous lecture into practice.
There are two written tests, one after week eight on foundations, data and reinforcement learning, and one after week fourteen on imitation learning, VLA and evaluation. The assignment is a pod project where you take a pick-and-place task through the whole cycle and demonstrate it live. Every lesson starts with a short check on the previous one, so keep up week by week.

## Slide 21: Activity: Spot the stage
In pairs, label each card with a lifecycle stage and the method it belongs to (RL, IL or VLA).
“A student hand-guides the leader arm fifty times.”
Answer: Collect data · IL
“4,096 simulated arms try to reach a target.”
Answer: Train · RL
“The policy succeeds 14 times out of 20 on the real arm.”
Answer: Evaluate · any
“Each demo is saved with ‘pick the blue cube’.”
Answer: Collect data · VLA
10 minutes · 8 cards per pair · answers shown on screen afterwards
Notes: Time to check understanding. In pairs, take the eight scenario cards and label each one with the lifecycle stage it belongs to and the method it belongs to. Four example cards are on the slide.
Instructor: hide the answer lines (or print cards without them) before class, and reveal them after the discussion. Listen for pairs who confuse collecting data with training; that is the most common mix-up at this stage.

## Slide 22: Exit ticket
Answer on paper or in the form before you leave:
  What does the SO-101 policy receive as its observation each step?
  What does it output as its action?
  Put the six lifecycle stages in order.
  Where does reinforcement learning get its training data?
  Where does imitation learning get its training data?
Notes: Before you go, five quick questions. They match the learning outcomes from the start of the lesson. If you are unsure about any of them, that is fine; it tells me what to revisit at the start of next week's lab.
Instructor: review the answers before Lesson 2 and use the most-missed question as the lab's entry check.

## Slide 23: Next week: L2 lab · Meet the tools
Sim station · Isaac Sim
Tour the simulator
Load the SO-101 and move each joint
Watch a trained Reach policy
Arm station · SO-101
Calibrate leader and follower
Teleoperate with live camera view
Fill in the joint table
Safety first: clear workspace, hands out of the follower's path, cut the power (not just USB) to stop, never leave a powered arm alone.
Notes: Next week is our first lab. You will rotate between two stations. At the sim station you will tour Isaac Sim, load the SO-101 and watch a policy trained with reinforcement learning, which you will train yourselves in Lesson 6. At the arm station you will calibrate the leader and follower and teleoperate them.
Safety starts next week. Keep the workspace clear, keep your hands out of the follower's path, and if anything goes wrong, cut the power supply, not just the USB cable. Never leave a powered arm on its own. See you in the lab.

## Slide 24: References and further reading
Capuano et al. (2025). Robot Learning: A Tutorial. https://arxiv.org/abs/2510.12403
Hugging Face LeRobot documentation: SO-101. https://huggingface.co/docs/lerobot/so101
NVIDIA. Train an SO-101 Robot From Sim-to-Real With NVIDIA Isaac. https://docs.nvidia.com/learning/physical-ai/sim-to-real-so-101/latest/index.html
Zhao et al. (2023). Learning Fine-Grained Bimanual Manipulation with Low-Cost Hardware (ACT). https://arxiv.org/abs/2304.13705
Rudin et al. (2021). Learning to Walk in Minutes Using Massively Parallel Deep RL. https://arxiv.org/abs/2109.11978
Lynch & Park. Modern Robotics (free book and videos). https://hades.mech.northwestern.edu/index.php/Modern_Robotics
Notes: These are the main sources behind today's lecture. The Robot Learning tutorial from Hugging Face is the best single place to read more; sections one and two cover what we did today.